## Slide 1: RWANDA Labour Inspectors Training Programme in Bugesera 27th November to 1st December 2023
By: Peneyambeko Alina MUNKAWA
Occupational Safety and Health Specialist
ILO- DWT for Eastern and Southern Africa

## Slide 2
HAZARDOUS SECTORS AND VULNERABLE WORKERS

## Slide 3
Module 9: Dealing with vulnerable workers
COURSE FOCUS & DURATION (180 minutes: 60 + 120)

## Slide 4
High risk sectors
Facts, Definitions, Common hazards and challenges, Stake and duty holders, Inspection and Compliance, regarding:
Construction
Agriculture
Vulnerable workers
Characteristics of vulnerable workers
Facts, Definitions, Common hazards and challenges, Protection, regarding:
Young workers
Workers in Informal economy
COURSE OUTLINE

## Slide 5
Facts
At least 108 thousand workers are killed on site every year globally,
This makes up 30 per cent of all occupational fatal injuries.
In industrialized countries t construction workers are 3 to 4 times more likely than other workers to die from accidents at work.
In the developing world, the risks associated with construction work may be 3 to 6 times greater.
Many more workers suffer and die from occupational diseases arising from past exposure to dangerous substances, such as asbestos.
ILO, 2015
High risk sectors: Construction

## Slide 6
Facts
employs a significant number of mostly unskilled workers worldwide
outsource the supply of goods and services required in the production process
very diverse groups of stake & duty holders at different phases and in the supply chain
poor safety and health conditions on construction sites and along the entire supply chain
conflict between labour laws and procurement method
tight deadlines and delivery pressure
ILO, 2021
High risk sectors: Construction

## Slide 7
Construction value chain mapping
NB. Each of the seven stages can play a role in addressing OSH

## Slide 8
Stake and duty holders in Construction value chain: A Mayanmar picture

## Slide 9
Definitions (ILO Code of Practice OSH in Construction
High risk sectors: Construction
Client: Any natural or legal person for whom a project is carried out.
Competent authority: A minister, government department, or other public authority having the power to issue regulations, orders or other instructions having the force of law.
Contractor: A person or enterprise providing services to an employer in accordance with national laws and regulations, or with agreed specifications, terms and conditions. For the purpose of this code of practice, contractors include principal contractors and labour supply agents.
Construction project: A construction project is the organized process of constructing, renovating, refurbishing, etc. a building, structure or infrastructure. This includes the planning, procurement, design, implementation and handover phases as well as the construction site.

## Slide 10
Definitions (ILO Code of Practice OSH in Construction
High risk sectors: Construction
Construction: activity that involves:
building, including excavation and the construction, structural alteration, renovation, repair, maintenance (including cleaning and painting) and demolition of all types of buildings or structures;
civil engineering, including excavation and the construction, structural alteration, repair, maintenance and demolition of, for example, airports, docks, harbours, inland waterways, dams, river and avalanche and sea defence works, roads and highways, railways, bridges, tunnels, viaducts and works related to the provision of services such as communications, drainage, sewerage, water and energy supplies;
the erection and dismantling of prefabricated buildings and structures, as well as the manufacturing of prefabricated elements on the construction site; and
the fabrication and erection of oil rigs and of offshore installations while under construction on shore.

## Slide 11
Definitions (ILO Code of Practice OSH in Construction
High risk sectors: Construction
Construction site: is where any of the above processes or operations are carried on.
Employer: Any physical or legal person who employs one or more workers on a construction site; and as the context requires, the principal contractor, the contractor or the subcontractor
Principal contractor: a person or body with actual control over or primary responsibility for overall construction site activities.
Worker: Any person engaged in construction.
Workplace: All places where workers need to be or to go by reason of their work and which are under the control of an employer as defined in “employer”.

## Slide 12
producing unique products (a building, a bridge, a road, etc.)
different and/or conflicting interests:
owners/clients (low cost, high quality);
users (high quality of life, comfort);
designers (aesthetics, structural safety);
contractor and subcontractors (reduce costs, improve productivity)
high number of subcontracting and outsourcing
micro or small enterprises as subcontractors/employers
payment on the basis of “work performed”
Construction: Common challenges

## Slide 13
Construction: Common hazards

## Slide 14
Common of construction accidents

## Slide 15
Initiatives for inspection and compliance in Construction
1. Contractor and subcontractor management
introducing limitation into their national laws or regulations, e.g. limiting it to 3 levels, with the first level being the subcontractor of the constructor or the main constructor.
requiring the contractor to be the constructor
setting a minimum number of permanent construction workers that a construction firm may employ
requiring at every construction site, the contractors to keep and maintain a record of all subcontractors

## Slide 16
Initiatives for inspection and compliance in Construction
2. Prior notice of a construction project indicating among others:
Client(s) including name(s) and address(es);
Exact address of the construction site
Date planned for start of work on the construction site;
Project supervisor(s) including name(s) and address(es)
Coordinator(s) for OSH during the project preparation stage (design phase) and execution stage including name(s) and address(es);
Planned number of contractors and self-employed persons on the construction site;
Estimated maximum number of workers on the construction site;
Details of contractors already chosen.

## Slide 17
Initiatives for inspection and compliance in Construction
3. Planning an OSH inspection programme for two groups: Construction sites and Construction enterprises
Criteria for selecting construction sites to be inspected
based on the information contained in the Prior Notice
types of work;
types of particular risk.
Criteria for selecting construction enterprises to be inspected
analysis of the occupational accident statistics of each enterprise;
analysis of all the evaluations of the construction sites of each enterprise.

## Slide 18
Initiatives for inspection and compliance in Construction
4. OSH organisation of construction enterprises and sites:
Some countries
classify construction enterprises by the number of workers employed: micro (fewer than 10 workers), small (10 to 49 workers), medium (50 to 249 workers) and large (250 or more workers).
require construction enterprises with 50 or more workers to organise in-house OSH services at each workplace
require OSH organization of construction sites to include specific number and expertise of the OSH experts depending on risks, the size of the construction site, also complexity and type of construction works running at the same time.

## Slide 19: Activities (25 + 20 minutes)
Activity 1: Who should have done what to prevent the collapse of the building? Is such duty provided for by Rwanda’s law/s?
Materials:
1. ILO Code of Practice on OSH in Construction:
Duties of Competent Authorities: Page 13-17
Duties of Employers: Page 19-23
Duties of the Clients: Page 25-28
Duties of designers, engineers, architects, suppliers, and manufacturers: Page 28
Procurement and contracting: Page 43-44
Performance monitoring and evaluation: Page 44-45
2. Kenya case: Architects blame corruption and lack of regulation.
NB. Try to speak to as many of the underlined words/phrases as possible.
3. Laptop/flip chart, marker
Group 1
Group 2
Group 3
Group 4

## Slide 20
High risk sectors: Agriculture
Common hazards
Agriculture is one of the most hazardous sectors in both the developing and industrialized countries.
Hazards in agricultural sector include:
Machinery, Ergonomics, Agricultural installations, and Chemicals
Exposure to pesticides and other agrochemicals
Long hours of work.
Work in the open: exposure to wind, rain, cold, heat and ultraviolet radiation.

## Slide 21
High risk sectors: Agriculture
Common challenges
Child labour in agriculture accounts for approximately 70 per cent of child labour worldwide (ILO, 2011)
Seasonal, migrant and casual labourers are common in agriculture sector
Poor recording and notification of injuries and diseases
High rates of fatalities and injuries ---- related to machinery such as tractors
Agricultural workers often live at place of work: clean water, accommodation and sanitation deficits

## Slide 22
Agriculture: Hazards
1. Machinery and equipment: tractors, cultivators, sprayers, etc.
Injuries: cuts, burns, electrocution, fractures and amputations
2. Ergonomics and the handling of materials: stooping, reaching, bending, and carrying out repetitive movements in awkward body positions
lower back injury, cumulative trauma disorders, neck and upper extremity impairment,
3. Chemicals: Pesticides, fertilizers, veterinary medicines, gases, vapours
acute toxicity syndrome, irreversible damage to the lungs, dermatitis
4. Noise: from farm equipment or animal production
Hearing loss

## Slide 23
Agriculture: Hazards
5. Dusts and particulate matters : from grains, legumes and other field crops.
injury to the lung, asthma, organic dust toxic syndrome, “farmer’s lung”.
6. Animal wastes: manure and waste slurry
dizziness, headache, severe breathing problems, convulsions
7. Zoonoses: infected animal or animal by-products, raw or undercooked animal products or contaminated milk, or drinking water
infectious diarrhoea, influenza, pneumonia, anthrax, rabies
8. Weather factors: hot or cold working environments,
Heat stress is associated with heat stroke, heat exhaustion, dehydration, cold stress, hypothermia

## Slide 24
Government and Inspectorate-led initiatives
1. Outreach and education campaigns:
raising general public awareness and promotion of OSH culture amongst individual workers, such as migrant and seasonal workers and those in the informal economy
involving government sponsored agencies such as OSH information and advice centres,
Involving private sector, including employers, workers and their organizations, trade associations, manufacturers and suppliers of equipment and products.
Involving NGOs and educational/ training organizations

## Slide 25
Government and Inspectorate-led initiatives
Outreach and education campaigns might make use of rural promoters and instructors for:
– the distribution of posters, pamphlets, periodicals and newspapers;
– organization of film shows, radio and TV broadcasts;
exhibitions and practical demonstrations on
hygiene and safety;
– organization of OSH conferences;
–workers’ education programmes; and
– arrangements of lectures, debates, seminars and competitions

## Slide 26
Vulnerable workers

## Slide 27
Vulnerability is often related to their gender or age
Economically, socially and/or politically marginalized
Physical, geographical, social or cultural isolation
Subject to discrimination, psychosocial pressures, abuse or harassment (disability, HIV status, etc)
Poorly organized and represented by trade unions or other workers’ organizations
Engaged in 3-D jobs dirty, degrading and dangerous
Commonly found in hazardous sectors, such as construction, mining, agriculture and fishing
At greater risk of work-related accidents and ill-health
Sometimes less accessible by labour inspection services
Characteristics of vulnerable workers

## Slide 28
Definitions:
Child labour comprises work that children are too young to perform and/or work that, by its nature or circumstances, is likely to harm children’s health, safety or morals.
Permitted light work is the work permitted by national laws or regulations for the persons from 13 years of age (or 12 years in countries that have specified the general minimum working age as 14 years) in light work that is not likely to harm their health or development, or cause limit school attendance, participation in vocational orientation or training programmes, or the capacity to benefit from instruction.
Hazardous work refers to work that, by its nature or circumstances, is likely to harm children’s health, safety or morals.
Young workers are those within the age group of 15 to 24 years.
Vulnerable workers: Young workers

## Slide 29
1. Protecting Young Workers’ Safety and Health through OSH Legislation
Requiring in OSH legislation protection of the physical and mental health of all workers, including young people working in the informal economy
Developing a List of Hazardous Works Prohibited for Young Workers under 18 (ILO Convention Worst Forms of Child Labour Convention No. 182)
Including in OSH laws special requirements for employers regarding training and information on OSH when hiring a new worker or an apprentice
Role of Government

## Slide 30
1. Protecting Young Workers’ Safety and Health through OSH Legislation
d. Providing for special protection of the health, safety and morale of young workers through minimal requirements, such as:
prohibiting night work;
limiting maximum working time;
providing adequate daily, weekly and annual periods of rest; and
ensuring that working time does not adversely affect the ability to benefit from education.
Role of Government

## Slide 31
1. Protecting Young Workers’ Safety and Health through OSH Legislation
e. Promoting Compliance with OSH Legislation to Better Protect Young Workers
Compliance strategy for all role players: judicial system, the labour inspectorate, employers and their associations, workers’ organizations, young workers, youth associations, and the education system.
Data and research on OSH and young workers through reporting and notification of fatal and non-fatal occupational injuries, occupational diseases
Role of Government

## Slide 32
2. Improving Education and Raising Awareness
OSH issues in: school curricula at various levels, vocational training and in initial training in the workplace.
Intensity of addressing young worker’s issues in OSH programmes and actions delivered by government, workers’ and employers’ organizations.
Singapore: mainstream safety and health education in primary and secondary schools. Programme target children between the age of 7 and 16, as well as (teachers, cleaners, operation managers, etc.)
Role of Government

## Slide 33
3. Improving OSH Regulations and Compliance
developing tools and guidelines to inform employers on OSH for young workers;
providing training and tools to labour/OSH administration, relevant local government agencies and other role players to support the implementation of the OSH/youth regulations.
publicizing major violations of OSH requirements: costs to worker safety and health, and the sanctions or penalties imposed
Role of Government

## Slide 34
4. Strengthening the Labour Inspection Role in Protecting Young Workers’ Safety and Health
Enhance competence of labour inspectors to recognize and address any situations of child labour, including hazardous child labour during any inspection visit.
Provide for and formalize inter-agency collaboration: labour inspectors, ministries of education, social services and health, as well as employers’ and workers’ organizations, teachers, NGOs, the community and parents.
Netherland: Every year the Labour Inspectorate carries out a holiday work programme focusing on industries where many young people and students do paid work.
Role of Government

## Slide 35
Vulnerable workers: Workers in Informal Economy
Informal economy: ‘informal economy’ refers to “ all economic activities by workers and economic units that are - in law or in practice - not covered or insufficiently covered by formal arrangements; and does not cover illicit activities, in particular the provision of services or the production, sale, possession or use of goods forbidden by law, including the illicit production and trafficking of drugs, the illicit manufacturing of and trafficking in firearms, trafficking in persons, and money laundering, as defined in the relevant international treaties”. (ILO)

## Slide 36: Informal Economy

## Slide 37
Vulnerable workers: Workers in Informal Economy
In some countries: the term carries same meaning as the “underground”, “shadow” or “grey” economy.
In others, same as Small and Medium Enterprises (SMEs)
Often not in conformity with legal requirements, e.g.--registration requirements
Considered as a natural and flexible “shock absorber”
Absorbs workers made redundant by formal structures
Often produces legal, low-priced and accessible goods and services for poor consumers
Makes up 85.8 per cent of employment in Africa

## Slide 38
Prevailing conditions: Workers in Informal Economy
hazardous jobs,
units are small-scale,
engaging mainly non-waged and unorganised workers
precarious work processes and labour arrangements,
largely unregulated and unregistered,
falling outside of state regulations and control, especially OSH and social protection,
lacking necessary awareness, technical means and resources for OSH
vulnerable to diseases and poor health.

## Slide 39: How OSH inspection can reach informal economy
Rethink the traditional functions and methods of work of labour administration.
Develop strategies for and commit resources to OSH programmes for informal sector.
Develop information and awareness raising campaigns with focus on advice on cheaper ways to comply with the law e.g. participatory action-oriented approach training (PAOT),
Encourage organization of MSEs and their workers, it is essential to finding solutions to their specific problems.
Improve data and knowledge of informality in a country contexts, for policy development.

## Slide 40: Direct roles of OSH Inspectorate
In consultation with informal economy/SMEs representatives, devise and promote measures to minimize hazards:
providing information on preventive measures, safe workplace behaviour;
developing freely accessible and easily understandable communication materials;
ensuring workplace hygiene and disinfection of premises,
identifying and equipping/re-organizing risk areas

## Slide 41: Direct roles of OSH Inspectorate
In consultation with informal economy/SMEs representatives, develop sector- and occupation-specific health guidelines, covering risk mapping and assessment, and OSH promotion progranne
Cooperate and collaborate with relevant authorities, e.g. public health, municipal, etc. and relevant representatives in inspection
Facilitate access to and correct use of PPEs.

## Slide 42: Some of adaptable ILO programme for informal economy/SMEs
Work Adjustment for Recycling and Managing Waste (WARM)
Agriculture: Work Improvement in Neighbourhood Development (WIND),
Work Improvement in Small Construction Sites (WISCON),
Work Improvement in Small Enterprises (WISE),
in Small Enterprises (WISE-R), and
Work Improvement for Safe Home (WISH).

## Slide 43: Thank you